## Slide 1
July 2019
SCTL55 Smart Configurator
Industry 4.0 in your hands

## Slide 2
Contents
SCTL55
Smart Configurator

## Slide 3
Contents
INTRODUCTION
Basically Technically information
Expectations
Markets of interest
THE PRODUCT
Relevant technical data
Product vs. price positioning
THE MARKET
Relevant applications
Marketing tools
CONCLUSIONS

## Slide 4
Introduction
Introduction
The SCTL55 Smart Configurator is a portable, self-powered and user-friendly device that allows to configure IO-Link sensors in an extremely easy way and replaces the need to program the sensor via a USB IO-Link Master connected to a PC with a dedicated software or via a network connected master device.
Full mobility, thanks to the rechargeable high capacity battery that lasts more than 5 hours in full operation and more than 22 hours with the screen off. It can be used on the plant floor or in the office without the need for power or a laptop.
Monitor sensor status and diagnostic. Through the 5.5" HD touchscreen display and a dedicated App you can now access to an advanced diagnostic, check operating hours, number of detections, operating cycles, alarms and much more. You can verify your sensor status, including current temperature, quality of run and process data and easily change the operating sensor parameters, such as switch point mode, sensing distance, timing functions, output configuration (PNP/NPN/push-pull, NO/NC), to better meet the process requirements.
Basic Technical information

## Slide 5
As soon as you plug the sensor to one of the 3 connectors on the top of the device, if IODD file is not already memorized, the SCTL55 will automatically download it, through Wi-fi and show all sensor’s data in a few seconds.
Thanks to the user friendly GUI, it is so easy for the users to add any parameter to favourite selection on the homepage and create profiles with different levels of accessibility to the sensor’s parameters as observer, maintainer or specialist.
Basic Technical information

## Slide 6
Introduction
Introduction
This unique device makes Carlo Gavazzi be recognized as the technological leader in sensor’s diagnostic and programming, with a game-changing new product that nobody else have available in its product range. The new Smart Configurator is a really user friendly, wireless solution that simplifies the configuration, adjustment and diagnosis of an IO-Link sensor, also installed on a machine.
Thanks to this new device we expect Carlo Gavazzi to be recognized as one of the main players in Industry 4.0.
Expectations

## Slide 7
Small and Medium size Machine / Distributors
Large Machine and Process
Simplify system design
Simplify maintenance
Use all IO Link features
Configurable sensor on the machine
Less inventory
Easy to use, flexible and portable
Introduction
Markets of interest

## Slide 8
The product
Display type
T: Touch screen
S C
55
T L
Smart Configurator
Type of connectors
L: 1 x M8 3-wire, 1 x M8 4-wire, 1 x M12
Relevant Technical Data
Type code for standard product
Screen size
55: 5.5” HD diplay

## Slide 9
5.5” HD touch screen display 720 x 1280 pixels
Body in polycarbonate, IP30
Internal memory and microSD card expandable memory
Wi-Fi enabled (b,g,n)
Micro USB port
High capacity rechargeable Li-ion battery
Possibility to recharge the battery with a power bank
LED indicators for the main battery
Lanyard and belt clip for portability
Transportation bag
The product
Relevant Technical Data

## Slide 10
Supply voltage: 24VDC +/- 20%
Max load: 80mA / short circuit protected
SIO2 output test: Led indicated Standard IO 2 logic state (pull down only)
Incorrect polarity protection
Connectors to sensors:
  Plug type: M8 3-wire, M8 4-wire, M12
  Cable type: connect via accessory (included)
IO-Link protocol support: IO-Link v1.1
The product
Relevant Technical Data: IO-Link interface

## Slide 11
Carlo Gavazzi launcher homepage and app store
Dimensions (H x L x W): 62 x 222 x 90 mm
Ambient air temperature:
  Charging: 10 to +35°C
  Operating: 0 to +40°C
Storage temperature: 0 to +50°C
The product
Relevant Technical Data

## Slide 12
Short press for main battery status
The product
System and battery LEDs
HD Touch screen display
For future use
Power On
Micro SD card port
User interface
Micro USB port

## Slide 13
The product
Rechargeable high capacity battery
Operating time:
  Full operation: > 5 hours
  Screen off: > 22 hours
Standby time:
  Device completely off: 6 months
LI-ION Internal batteries:
  3.8V / 10Ah (2x3.5Ah + 3Ah)
Charge time:
  5V / 1A standard charger via USB mini connector: < 10 hours

## Slide 14
The product
LEDs
Battery status
IO-Link
Error
SIO2
USB
Power

## Slide 15
The product
LEDs

## Slide 16
The product
LEDs

## Slide 17
The product
LEDs

## Slide 18
The product
Connectors to connect Plug-version sensors
M12
M8 3-wire
M8 4-wire

## Slide 19
The product
Extension cable to connect cable-version sensors
0.5m M12 to 4 hooks, marked with different colors

## Slide 20
The product
Gestures
TOUCH
SWIPE

## Slide 21
The product
Home page
Setting
«Configure» App
Carlo Gavazzi App store
Wi-Fi switch

## Slide 22
The product
Wi-Fi setting

## Slide 23
The product
Software update

## Slide 24
The product
Play the «Configure» APP

## Slide 25
The product
Connect your sensor – IODD file not present on the device

## Slide 26
The product
Automatic download of IODD file and sensor configured

## Slide 27
The product
«Configure» app homepage
Parameterization
Exit the App
Basic information of the sensor connected
Process DATA
Graphic of the set point
Main icons
Favourite parameters

## Slide 28
The product
Parameterization
Information on the sensor connected
Load config. file
Save config. file
Settings
Exit the App
User profile
Tab selection

## Slide 29
The product
Creation of a new user

## Slide 30
The product
Access level to parameters for different user profiles

## Slide 31
The product
Configuration file management: save, load and write
Save, load and write a project
Delete, rename or load a project
List of project

## Slide 32
The product
IODD file
Delete or update the existing IODD files
Refresh the IODD index

## Slide 33
The product
Process data
Example of Switching Output active
Example of Switching Output active

## Slide 34
The product
Switching output setup
Select to change
Select to change
Command Icons

## Slide 35
The product
Command icons
1 step back
1 step forward
The changes are written into the sensor
Read the parameters from hthe sensor
In «Live mode» the changes are written automatically into the sensor

## Slide 36
The product
Add a parameter to the favourite list

## Slide 37
The product
Delete a parameter from the favourite list

## Slide 38
The product
Main icons: example with «Divider» function

## Slide 39
The product
Use case 1 - Parameterization of IO-Link sensors
Connect your sensor using one of the 3 connectors or with the extension cable
1
Scroll the parameters on the touch screen, chose the one you want to change and select the value among the multiple values proposed or by keying the value directly
2
Verify that the value is the one you need and write it into the sensor
3

## Slide 40
The product
Use case 2 – Initial commissioning of machines and plants
Connect the Smart Configurator directly to the sensor in the machine
1
Verify the behaviour of the sensor by reading the parameters and process data while the sensor is running
2
Adjust the sensor’s parameters to better fit the application
3

## Slide 41
The product
Use case 3 – Sensor performance verification
Connect the Smart Configurator directly to the capacitive sensor located in the machine
1
Check the operating hours, number of detection and the quality of run value, to verify the actual sensing performance of your device
2
Adjust the sensor and fine tune it on the machine or replace it with a new one
3

## Slide 42
Connect the Smart Configurator directly to the sensor located in the machine
1
Easy access to the IO-Link sensor’s process and diagnostic data to monitor the status
2
Read the frequency, the temperature and check alarms and events
3
The product
Use case 4 – Status monitoring of IO-Link sensors

## Slide 43
The product
Accessories
Lanyard
Extension cable
Micro USB cable
Protective holster

## Slide 44
Specifications | Carlo Gavazzi | IFM | P&F | Lemon Age | Sick | TMG
Model Name | SCTL55 | E30396 | Smart Bridge | IO-Fly | SiLink2Master | IO Link Device
Display | Yes | No | No | No | No | No
Platform | Stand alone | PC | Android, iOS | iOS | PC | PC
WiFi | Yes | No | No | Yes | No | No
Bluetooth | Future dev. | No | Yes | Yes | No | No
USB | Yes | Yes | No | Yes | Yes | Yes
Wired/Wireless | Wireless | Wired | Wireless | Wireless | Wired | Wired
Internal Memory | Yes | No | No | No | No | No
Expandable Memory | Yes | No | No | Yes | No | No
Self Powered | Yes | No | No | Yes | No | No
Software/App | Free | License | Free | Free | Free | Free
Wow Factor |  |  |  |  |  | 
The product

## Slide 45
Marketing Tools
Instruction manual
SCTL55 Smart Configurator
Available in: Chinese, Danish, English, French, German, Italian and Spanish
The market

## Slide 46
Marketing Tools
Product Brochure
SCTL55 Smart Configurator
Available in: English
The market

## Slide 47
Marketing Tools
Quick start guide
SCTL55 Smart Configurator
Multilanguage: Chinese, Danish, English, French, German, Italian and Spanish
The market

## Slide 48
The market
Certifications
EMC CFR 47 Parts 15.107 & 15.109
Radio CFR 47 Part 15 Subpart C
Contains FCC ID: 2AH8Q-HT17
EN62368-1
Radio ETSI EN 300 328 v2.1.1
General reference:

## Slide 49
Powerful diagnostic
5.5” HD touch screen display
Portability
High capacity battery
IODD automatic download via Wi-Fi
Conclusions
IO-Link
Easy and quick connection

## Slide 50
Thank you for your attention!